## Slide 1: Development of a Microvibration and Torque Measurement Device for Reaction Wheel Assemblies
Presenters: Brodie Cruse & Matthew McGill
Supervisor: Dr Guglielmo Aglietti
Department of Mechanical Engineering, University of Auckland
Notes: Introduce yourselves and the project name - no technical content yet.
One sentence on what the next 8 minutes will cover.
Keep energy up - this sets the tone for the whole talk.

## Slide 2: Problem Statement
RWAs are the primary attitude control actuator on satellites
During operation they generate microvibrations that degrade payload performance
Accurate characterisation of forces, torque, and imbalance is critical for mission success
De Munter et al. (2020): a 30 Hz structural mode excited by a reaction wheel caused 3 arcsec RMS pointing error
Image placeholder: satellite / RWA in orbit
Notes: Don't read the bullets - use the image to anchor the explanation.
Explain plainly what a reaction wheel does: it spins internally to torque the spacecraft without using fuel.
Even a well-balanced wheel isn't perfectly balanced - residual microvibrations leak straight through into the structure.
Use the De Munter number as the hook: a wheel exciting a 30 Hz structural mode caused 3 arcsec RMS pointing error - significant against a high-resolution imaging budget.
Land on: this is a measurement problem before it's a mitigation problem - you can't fix what you haven't characterised.

## Slide 3: Project Objective
Design and build a unified measurement device for RWA microvibrations, imbalance, and torque
Image placeholder: Kistler dynamometer table (commercial)
Image placeholder: our CAD - stinger measurement platform
~$10,000+ → ~$500 equivalent
Notes: State the objective as a single sentence - don't over-elaborate.
Let the $10k -> $500 comparison land as the "so what" - commercial-grade capability at a fraction of the cost.
Quick pivot line into the state-of-the-art slide.

## Slide 4: State of the Art
Approach | Why it's insufficient
Kistler dynamometer tables | Measure force/torque well, but no direct imbalance output; $10k+
Commercial balancing machines | Measure imbalance, but not force/torque disturbance spectra
Published models (e.g. Masterson) | Need per-wheel characterisation - no substitute for direct measurement
Gap: no single device measures force, imbalance, and torque together in one integrated device
Notes: Kistler tables measure force/torque well but don't give imbalance directly and cost $10k+.
Commercial balancing machines measure imbalance but not force/torque disturbance spectra.
Published models (e.g. Masterson) need per-wheel characterisation - no substitute for direct measurement.
Land clearly on the gap: nothing currently measures force, imbalance, and torque together in one integrated device.

## Slide 5: Measurement Requirements
Requirement | Target
Microvibrations | Force spectra across operating speed range
Static imbalance | < 26 g·mm (Rocket Lab flight spec)
Dynamic imbalance | < 800 g·mm² (Rocket Lab flight spec)
Torque | Spin-up / operational torque profile
Notes: Frame this as: before designing hardware, we needed numbers to design against.
Use Rocket Lab's flight qualification spec as a concrete, industry-grounded target - not an arbitrary number.
Close with a clean handoff: "that's the target - Matthew will take you through how we're hitting it".

## Slide 6: Concept Overview
Six-component measurement: 3 forces (Fx, Fy, Fz) + 3 torques (Tx, Ty, Tz) fully characterise a wheel's disturbance signature
First concept explored: a floating ring plate with bearings on a rotating ring
Rejected — preload sensitivity and mechanical complexity led to the stinger concept
Image placeholder: six-component force/torque diagram (Fx, Fy, Fz, Tx, Ty, Tz)
Image placeholder: ring plate concept sketch
Notes: Explain what "six-component" means physically: three forces + three torques fully characterise a wheel's disturbance signature.
Briefly mention the ring plate was the first concept explored - bearings on a rotating ring.
Rejected due to preload sensitivity and mechanical complexity - sets up why the stinger concept was chosen instead.
Keep this brief - it's a bridge into Matthew's decoupling problem slide, not a deep dive.

## Slide 7: Decoupling Problem
Radial and axial measurement must not interfere with each other
Stinger solves this — stiff in one direction, compliant in the other
Image placeholder: axial vs radial force direction diagram
Notes: Explain physically why cross-talk matters: if radial load bleeds into the axial channel, imbalance measurements get corrupted.
State the stinger principle in plain language - stiff in the direction you're measuring, floppy in the others.
Keep it brief, this is context for the concept comparison slide next.

## Slide 8: Ball Bearing vs. Stinger
Ball bearing plate: needs preload to stay seated — extra failure mode, extra complexity
Stinger: no pretensioning, clean single load path, only six components to manufacture and align
Image placeholder: ball bearing plate sketch
Image placeholder: stinger platform CAD
Notes: Ball bearing plate needed preload to stay seated - an extra failure mode and extra complexity.
Stinger needs no pretensioning, gives a clean single load path, and only six components to manufacture and align.
Let the CAD image do the work - don't over-narrate the sketch.

## Slide 9: Stinger Design Analysis
Image placeholder: stinger diagram (d, L labelled)
fn > 500 Hz
(one-third rule)
kax/klat > 3000
(cross-axis decoupling)
SFbuckle > 5
(buckling margin)
SFyield > 3
(yield margin)
Check | Target | Axial | Radial
fn [Hz] | > 500 | 892.1 ✓ | 515.0 ✓
kax/klat | > 3000 | 3333 ✓ | 3333 ✓
SFbuckle | > 5 | 100.9 ✓ | 241.7 ✓
SFyield | > 3 | 6.4 ✓ | 4671.6 ✓
Four checks per stinger, selected geometry: d = 2 mm, L = 50 mm, steel
Notes: Say plainly: four checks per stinger, all four passed for the selected geometry (d = 2 mm, L = 50 mm, steel).
Natural frequency > 500 Hz keeps the stinger's own resonance out of the measurement band (one-third rule: fn > 3x max measurement frequency).
Stiffness ratio > 3000 keeps axial and radial channels decoupled - cross-axis error under 0.03%.
Buckling and yield margins are comfortable at this diameter - steel is well within capability.
Don't derive the equations live - just say "we check four things to make sure the stingers work" and walk through the results table.

## Slide 10: FEA Modal Analysis
Image placeholder: FEA Mode 1 screenshot (plate_mass, ANSYS)
Mode | Description | Freq [Hz]
1 | Lateral translation – X | 334.5
2 | Lateral translation – Y | 396.8
3 | Torsion about Z | 696.4
4 | Axial bounce – Z | 892.7
5 | Rocking about X | 965.7
6 | Rocking about Y | 998.8
Modes 1 & 2 sit below the 500 Hz target due to radial-stinger support compliance — fix identified for Semester 2: stiffen radial stinger supports
Notes: Full 17-body assembly modal analysis in ANSYS - RWA represented as a 1.0 kg point mass at the rotor centre-of-mass height.
First six modes: two lateral translation (334 Hz, 397 Hz), torsion (696 Hz), axial bounce (893 Hz), two rocking modes (966 Hz, 999 Hz).
Be upfront: Modes 1 and 2 sit below the 500 Hz target - that's support compliance in the radial stingers, not a fundamental flaw.
Fix already identified: stiffen the radial stinger supports (increased wall thickness), planned as the first Semester 2 design iteration.
"Mode 1 is below target due to support compliance - we've identified the fix for Semester 2".

## Slide 11: Sensor Selection
Image placeholder: sensor photos (S-beam load cell / PCB 208C01 ICP)
Sensor | Channel | Role
3× S-beam strain gauge | Axial | High-precision static/low-frequency load
3× PCB 208C01 ICP | Radial | High-frequency microvibration bandwidth
Hybrid approach — each sensor type matched to its measurement role
Notes: Axial channel needs high-precision static/low-frequency load measurement - S-beam strain gauges suit that role.
Radial channel carries the higher-frequency microvibration content - ICP piezoelectric (PCB 208C01) is built for that bandwidth.
One line: each sensor type is matched to the physics of what it measures, not a single one-size-fits-all sensor.

## Slide 12: Next Steps
1
Sensor
procurement
2
Static
FEA
3
Detailed
design
4
Fabrication
5
Experimental
validation
Semester 2 (August – October 2026)
Target: working proof of concept by October 2026
Notes: Walk through the five-step path: sensor procurement -> static FEA -> detailed design -> fabrication -> validation.
Say the key dates out loud briefly - don't just point at the Gantt and move on.
End confidently: "by October we will have a working proof of concept".